## Slide 1: Testing Water
Dissolved Oxygen (DO).
Biochemical Oxygen Demand (BOD).
Chemical Oxygen Demand (COD)

## Slide 2: Control Measures for Water Pollution
Scientific Technique must be adopted in the Environment
Industry must recycle the water and use.
Plants and Trees are the natural air conditioners.
Forest are the reasons for controlling the SO2 CO2
Domestic Sewage must be used for Irrigation.

## Slide 3: Control Measures for Water Pollution
Public awareness must be created.
Framing of Laws and must be modified according to the technological development.

## Slide 4: Waste Water Treatment
Objectives
  To convert harmful component to harmless components.
  To eliminate the offensive smell.
  To remove the solid content of the sewage.
  To destroy disease producing bacteria.

## Slide 5: Waste Water Treatment
Treatment process
Primary Treatment
Secondary Treatment
Tertiary Treatment
Disposal
of
Sewage

## Slide 6: Waste Water Treatment
Primary Treatment
  Settling process.
  Large Quantity of organic and inorganic materials removed in this process.
  The settling coagulants ( Alum, Ferrous Sulphates ) are added and suspended particles are converted in to settlements.
  Al2(SO4)3 + 6H2O  2Al(OH)3 ↓ + 3H2SO4

## Slide 7: Waste Water Treatment
Secondary Treatment
  In this process organic impurities removed by aerobic bacteria.
  90 % of Oxygen Demanding Wastes are removed.
  To Process
    Trickling Filter.
    Activated Sludge Process.

## Slide 8: Waste Water Treatment
Trickling Filter Process

## Slide 9: Waste Water Treatment
Trickling Filter Process
  Tank is filled with coarse or crushed rock.
  Sewage is sprayed over the bed by rotating arms.
  Sewage is penetrated through bed.
  Filtering material ( aerobic bacteria ) use the sewage as food.
  After completion of this process 80 to 85 % of BOD is removed

## Slide 10: Waste Water Treatment
Activated Sludge Process.
Aeration Tank
Sedimentation
Tank
Sludge Settled at the bottom
Sewage
Effluent
From primary
Treatment
Activated
Sludge
Effluent
For drainage
Excess
Sludge
Air Supply

## Slide 11: Waste Water Treatment
Activated Sludge Process.

## Slide 12: Waste Water Treatment
Tertiary Treatment
  After Secondary Process BOD level comes to 25ppm.
  Effluent is introduced to flocculation tank.
  Lime is added to remove phosphates.
  Ammonia is removed in the form of gas.
  Finally passed through charcoal to filter minute organic maters.
  Finally water is treated with disinfectant(chlorine).

## Slide 13: Waste Water Treatment
Disposal of Sewage
  Dumping into low lying Areas.
  Burning of Sludge.
  Dumping into sea.
  Use it as lo grade fertilizers.